## Slide 1
Computer System Architectures
Chapter 3
Based on
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 3 :: Topics
Introduction
Latches and Flip-Flops
Synchronous Logic Design
Finite State Machines
Timing of Sequential Logic
Parallelism
Notes: In this chapter, we will analyze and design sequential logic.

## Slide 3
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about a circuit necessary to explain its future behavior
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: combinational logic followed by a bank of flip-flops
Introduction
Notes: The outputs of sequential logic depend on both current and prior input values. Hence, sequential logic has memory.
Sequential logic might explicitly remember certain previous inputs,
or it might distill the prior inputs into a smaller amount of information called the state of the system.
The state of a digital sequential circuit is a set of bits called state variables that contain all
the information about the past necessary to explain the future behavior of the circuit.

## Slide 4
Give sequence to events
Have memory (short-term)
Use feedback from output to input to store information
Sequential Circuits

## Slide 5
The state of a circuit influences its future behavior
State elements store state
  Bistable circuit
  SR Latch
  D Latch
  D Flip-flop
State Elements

## Slide 6
Fundamental building block of other state elements
Two outputs: Q, Q
No inputs
Bistable Circuit
Notes: The fundamental building block of memory is a bistable element, an element with two stable states. Figures show a simple bistable element consisting of a pair of inverters connected in a loop. The inverters are cross-coupled, meaning that the input of I1 is the output of I2 and vice versa.

## Slide 7
Consider the two possible cases:
  Q = 0:
  then Q = 1, Q = 0 (consistent)
  Q = 1:
  then Q = 0, Q = 1 (consistent)
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state
Bistable Circuit Analysis
Notes: Because the cross-coupled inverters have two stable states, Q = 0 and Q = 1, the circuit is said to be bistable. An element with N stable states conveys log2 N bits of information, so a bistable element stores one bit.

## Slide 8
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1
SR (Set/Reset) Latch
Notes: One of the simplest sequential circuits is the SR latch, which is composed of two cross-coupled NOR gates.
The latch has two inputs, S and R, and two outputs, Q and Q:
The SR latch is similar to the cross-coupled inverters, but its state can be controlled through the S and R inputs, which set and reset the output Q.

## Slide 9
  S = 1, R = 0:
  then Q = 1 and Q = 0
  S = 0, R = 1:
  then Q = 1 and Q = 0
SR Latch Analysis

## Slide 10
  S = 0, R = 0:
  then Q = Qprev
  S = 1, R = 1:
  then Q = 0, Q = 0
SR Latch Analysis

## Slide 11
  S = 0, R = 0:
  then Q = Qprev
  Memory!
  S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid State
  Q ≠ NOT Q
SR Latch Analysis

## Slide 12
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1
  (S = 1, R = 0, Q = 1)
  Reset: Make the output 0
  (S = 0, R = 1, Q = 0)
Must do something to avoid
invalid state (when S = R = 1)
SR Latch Symbol
Notes: Like the cross-coupled inverters, the SR latch is a bistable element with one bit of state stored in Q.
However, the state can be controlled through the S and R inputs.

## Slide 13
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1,
  D passes through to Q (transparent)
  When CLK = 0,
  Q holds its previous value (opaque)
Avoids invalid case when
Q ≠ NOT Q
D Latch
Notes: The D latch has two inputs.
The data input, D, controls what the next state should be.
The clock input, CLK, controls when the state should change.
The clock controls when data flows through the latch.
When CLK = 1, the latch is transparent.
The data at D flows through to Q as if the latch were just a buffer.
When CLK = 0, the latch is opaque.
It blocks the new data from flowing through to Q, and Q retains the old value.
Hence, the D latch is sometimes called a transparent latch or a level-sensitive latch.

## Slide 14
D Latch Internal Circuit

## Slide 15
D Latch Internal Circuit

## Slide 16
Inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered
Activated on the clock edge
D Flip-Flop

## Slide 17
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q
D Flip-Flop Internal Circuit
Notes: A D flip-flop can be built from two back-to-back D latches controlled by complementary clocks, as shown in Figure
The first latch, L1, is called the master. The second latch, L2, is called the slave.
A D flip-flop copies D to Q on the rising edge of the clock, and remembers its state at all other times.
The rising edge of the clock is often just called the clock edge for brevity.
The D input specifies what the new state will be.
The clock edge indicates when the state should be updated.

## Slide 18
D Latch vs. D Flip-Flop
Notes: A D flip-flop is also known as a master-slave flip-flop, an edge-triggered flip-flop, or a positive edge-triggered flip-flop.
The triangle in the symbols denotes an edge-triggered clock input.

## Slide 19
D Latch vs. D Flip-Flop

## Slide 20
Registers
Notes: An N-bit register is a bank of N flip-flops that share a common CLK input, so that all bits of the register are updated at the same time.

## Slide 21
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
Enabled Flip-Flops
Notes: An enabled flip-flop adds another input called EN or ENABLE to determine whether data is loaded on the clock edge.
When EN is TRUE, the enabled flip-flop behaves like an ordinary D flip-flop.
When EN is FALSE, the enabled flip-flop ignores the clock and retains its state.

## Slide 22
Inputs: CLK, D, Reset
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Resettable Flip-Flops
Notes: A resettable flip-flop adds another input called RESET. When RESET is FALSE, the resettable flip-flop behaves like an ordinary D flip-flop.
When RESET is TRUE, the resettable flip-flop ignores D and resets the output to 0.

## Slide 23
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 24
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 25
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves as ordinary D flip-flop
Settable Flip-Flops

## Slide 26
Sequential circuits: all circuits that aren’t combinational
A problematic circuit:
Sequential Logic

## Slide 27
Sequential circuits: all circuits that aren’t combinational
A problematic circuit:
No inputs and 1-3 outputs
Astable circuit, oscillates
Period depends on inverter delay
It has a cyclic path: output fed back to input
Sequential Logic
Notes: Suppose node X is initially 0. Then Y= 1, Z=0, and hence X= 1, which is inconsistent with our original assumption.
The circuit has no stable states and is said to be unstable or astable.
This circuit is called a ring oscillator.

## Slide 28
Breaks cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge: system synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock signal
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines
Synchronous Sequential Logic Design
Notes: Sequential circuits with cyclic paths can have undesirable races or unstable behavior.
To avoid these problems, designers break the cyclic paths by inserting registers somewhere in the path.
This transforms the circuit into a collection of combinational logic and registers.
The registers contain the state of the system, which changes only at the clock edge, so we say the state is synchronized to the clock.
If the clock is sufficiently slow, so that the inputs to all registers settle before the next clock edge, all races are eliminated.
The rules of synchronous sequential circuit composition teach us that a circuit is a synchronous sequential circuit if it consists of interconnected
circuit elements such that
Every circuit element is either a register or a combinational circuit
At least one circuit element is a register
All registers receive the same clock signal
Every cyclic path contains at least one register.
Sequential circuits that are not synchronous are called asynchronous.
Two other common types of synchronous sequential circuits are called finite state machines and pipelines.

## Slide 29
Consists of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
    Computes the outputs
Finite State Machine (FSM)
Notes: An FSM has M inputs, N outputs, and k bits of state.
It also receives a clock and, optionally, a reset signal.
An FSM consists of two blocks of combinational logic, next state logic and output logic, and a register that stores the state.

## Slide 30
Next state determined by current state and inputs
Two types of finite state machines differ in output logic:
  Moore FSM: outputs depend only on current state
  Mealy FSM: outputs depend on current state and inputs
Finite State Machines (FSMs)
Notes: There are two general classes of finite state machines, characterized by their functional specifications.
In Moore machines, the outputs depend only on the current state of the machine.
In Mealy machines, the outputs depend on both the current state and the current inputs.

## Slide 31
Traffic light controller
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB
FSM Example

## Slide 32
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB
FSM Black Box

## Slide 33
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 34
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 35
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | 
S0 | 1 | X | 
S1 | X | X | 
S2 | X | 0 | 
S2 | X | 1 | 
S3 | X | X | 
FSM State Transition Table

## Slide 36
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
FSM State Transition Table

## Slide 37
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X |  | 
0 | 0 | 1 | X |  | 
0 | 1 | X | X |  | 
1 | 0 | X | 0 |  | 
1 | 0 | X | 1 |  | 
1 | 1 | X | X |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
FSM Encoded State Transition Table

## Slide 38
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S'1 = S1 Å S0
S'0 = S1S0TA + S1S0TB
FSM Encoded State Transition Table

## Slide 39
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 |  |  |  | 
0 | 1 |  |  |  | 
1 | 0 |  |  |  | 
1 | 1 |  |  |  | 
Output | Encoding
green | 00
yellow | 01
red | 10
FSM Output Table

## Slide 40
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0
FSM Output Table

## Slide 41
FSM Schematic: State Register

## Slide 42
FSM Schematic: Next State Logic

## Slide 43
FSM Schematic: Output Logic

## Slide 44
FSM Timing Diagram

## Slide 45
Binary encoding:
  i.e., for four states, 00, 01, 10, 11
One-hot encoding
  One state bit per state
  Only one state bit HIGH at once
  i.e., for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler
FSM State Encoding
Notes: In the previous example, the state and output encodings were selected arbitrarily.
A different choice would have resulted in a different circuit.
One important decision in state encoding is the choice between binary encoding and one-hot encoding.
With binary encoding, as was used in the traffic light controller example, each state is represented as a binary number.
In one-hot encoding, a separate bit of state is used for each state.
It is called one-hot because only one bit is “hot” or TRUE at any time.
Each bit of state is stored in a flip-flop, so one-hot encoding requires more flip-flops than binary encoding.
However, with one-hot encoding, the next-state and output logic is often simpler, so fewer gates are required.
The best encoding choice depends on the specific FSM.

## Slide 46
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last two digits it has crawled over are 01. Design Moore and Mealy FSMs of the snail’s brain.
Moore vs. Mealy FSM

## Slide 47
Mealy FSM: arcs indicate input/output
State Transition Diagrams
Notes: Mealy machines are much like Moore machines, but the outputs can depend on inputs as well as the current state
Therefor, for Mealy machines, the outputs are labeled on the arcs instead of in the circles.

## Slide 48
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table

## Slide 49
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table
S1’ = S0A
S0’ = A

## Slide 50
Current State |  | Output
S1 | S0 | Y
0 | 0 | 
0 | 1 | 
1 | 0 | 
Y = S1
Moore FSM Output Table

## Slide 51
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
Y = S1
Moore FSM Output Table

## Slide 52
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
State | Encoding
S0 | 00
S1 | 01
Mealy FSM State Transition & Output Table

## Slide 53
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
State | Encoding
S0 | 00
S1 | 01
Mealy FSM State Transition & Output Table

## Slide 54
Moore FSM Schematic

## Slide 55
Mealy FSM Schematic

## Slide 56
Moore & Mealy Timing Diagram

## Slide 57
Break complex FSMs into smaller interacting FSMs
Example: Modify traffic light controller to have Parade Mode.
  Two more inputs: P, R
  When P = 1, enter Parade Mode & Bravado Blvd light stays green
  When R = 1, leave Parade Mode
Factoring State Machines
Notes: Designing complex FSMs is often easier if they can be broken down into multiple interacting simpler state machines such that the output of some
machines is the input of others. This application of hierarchy and modularity is called factoring of state machines.

## Slide 58
Unfactored FSM
Factored FSM
Parade FSM

## Slide 59
Unfactored FSM

## Slide 60
Factored FSM

## Slide 61
Identify inputs and outputs
Sketch state transition diagram
Write state transition table
Select state encodings
For Moore machine:
  Rewrite state transition table with state encodings
  Write output table
For a Mealy machine:
  Rewrite combined state transition and output table with state encodings
Write Boolean equations for next state and output logic
Sketch the circuit schematic
FSM Design Procedure
Notes: Finite state machines are a powerful way to systematically design sequential circuits from a written specification.
Use the following procedure to design an FSM:

## Slide 62
Flip-flop samples D at clock edge
D must be stable when sampled
Similar to a photograph, D must be stable around clock edge
If not, metastability can occur
Timing

## Slide 63
Setup time: tsetup = time before clock edge data must be stable (i.e. not changing)
Hold time: thold = time after clock edge data must be stable
Aperture time: ta = time around clock edge data must be stable (ta = tsetup + thold)
Input Timing Constraints

## Slide 64
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)
Output Timing Constraints
Notes: When the clock rises, the output (or outputs) may start to change after the clock-to-Q contamination delay, tccq , and must definitely settle to the final value within the clock to-Q propagation delay, tpcq .
These represent the fastest and slowest delays through the circuit, respectively.

## Slide 65
Synchronous sequential circuit inputs must be stable during aperture (setup and hold) time around clock edge
Specifically, inputs must be stable
  at least tsetup before the clock edge
  at least until thold after the clock edge
Dynamic Discipline
Notes: For the circuit to sample its input correctly, the input (or inputs) must have stabilized at least some setup time, t setup , before the rising edge of the clock and must remain stable for at least some hold time, t hold , after the rising edge of the clock.
The sum of the setup and hold times is called the aperture time of the circuit, because it is the total time for which the input must remain stable.

## Slide 66
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements
Dynamic Discipline

## Slide 67
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥
Setup Time Constraint

## Slide 68
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥ tpcq + tpd + tsetup
tpd ≤
Setup Time Constraint

## Slide 69
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)
Setup Time Constraint

## Slide 70
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold <
Hold Time Constraint

## Slide 71
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold < tccq + tcd
tcd >
Hold Time Constraint

## Slide 72
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold < tccq + tcd
tcd > thold - tccq
Hold Time Constraint

## Slide 73
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd =
tcd =
Setup time constraint:
Tc ≥
fc =
Hold time constraint:
tccq + tcd > thold ?
Timing Analysis

## Slide 74
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!
Timing Analysis
Notes: Because X′ did not hold stable long enough, the actual value of X is unpredictable.
The circuit has a hold time violation and may behave erratically at any clock frequency.

## Slide 75
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd =
tcd =
Setup time constraint:
Tc ≥
fc =
Hold time constraint:
tccq + tcd > thold ?
Timing Analysis
Add buffers to the short paths:

## Slide 76
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Timing Analysis
Add buffers to the short paths:

## Slide 77
The clock doesn’t arrive at all registers at same time
Skew: difference between two clock edges
Perform worst case analysis to guarantee dynamic discipline is not violated for any register – many registers in a system!
Clock Skew
Notes: In the previous analysis, we assumed that the clock reaches all registers at exactly the same time.
In reality, there is some variation in this time.
This variation in clock edges is called clock skew.
For example, the wires from the clock source to different registers may be of different lengths, resulting in slightly different delays.
When doing timing analysis, we consider the worst-case scenario, so that we can guarantee that the circuit will work under all circumstances.

## Slide 78
In the worst case, CLK2 is earlier than CLK1
Tc ≥
Setup Time Constraint with Skew

## Slide 79
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤
Setup Time Constraint with Skew

## Slide 80
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)
Setup Time Constraint with Skew

## Slide 81
In the worst case, CLK2 is later than CLK1
tccq + tcd >
Hold Time Constraint with Skew

## Slide 82
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd >
Hold Time Constraint with Skew

## Slide 83
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq
Hold Time Constraint with Skew

## Slide 84
Asynchronous (for example, user) inputs might violate the dynamic discipline
Violating the Dynamic Discipline
Notes: It is not always possible to guarantee that the input to a sequential circuit is stable during the aperture time, especially when the input arrives from the external world.
Consider a button connected to the input of a flip-flop, as shown in figure.
When the button is not pressed, D=0.
When the button is pressed, D =1.
A monkey presses the button at some random time relative to the rising edge of CLK.
We want to know the output Q after the rising edge of CLK.
In Case I, when the button is pressed much before CLK, Q =1.
In Case II, when the button is not pressed until long after CLK, Q =0.
But in Case III, when the button is pressed sometime between tsetup before CLK and thold after CLK,
the input violates the dynamic discipline and the output is undefined.

## Slide 85
Bistable devices: two stable states, and a metastable state between them
Flip-flop: two stable states (1 and 0) and one metastable state
If flip-flop lands in metastable state, could stay there for an undetermined amount of time
Metastability
Notes: When a flip-flop samples an input that is changing during its aperture, the output Q may momentarily take on a voltage between 0 and V DD
that is in the forbidden zone.
This is called a metastable state. Eventually, the flip-flop will resolve the output to a stable state of either 0 or 1.
However, the resolution time required to reach the stable state is unbounded.

## Slide 86
Token: Group of inputs processed to produce group of outputs
Latency: Time for one token to pass from start to end
Throughput: Number of tokens produced per unit time
Parallelism increases throughput
Parallelism Definitions
Notes: We define a token to be a group of inputs that are processed to produce a group of outputs.
The speed of a system is characterized by the latency and throughput of information moving through it.
The latency of a system is the time required for one token to pass through the system from start to end.
The throughput is the number of tokens that can be produced per unit time.

## Slide 87
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line
Parallelism
Notes: As you might imagine, the throughput can be improved by processing several tokens at the same time.
This is called parallelism, and it comes in two forms: spatial and temporal.
With spatial parallelism, multiple copies of the hardware are provided so that multiple tasks can be done at the same time.
With temporal parallelism, a task is broken into stages, like an assembly line.
Multiple tasks can be spread across the stages. Although each task must pass through all stages, a different task will be in each stage at any given time so multiple tasks can overlap. Temporal parallelism is commonly called pipelining.

## Slide 88
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Parallelism Example

## Slide 89
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour
Parallelism Example

## Slide 90
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa P. Hacker to help, using her own oven
  Temporal parallelism:
    two stages: rolling and baking
    He uses two trays
    While first batch is baking, he rolls the second batch, etc.
Parallelism Example

## Slide 91
Latency = ?
Throughput = ?
Spatial Parallelism

## Slide 92
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 2 trays/ 1/3 hour = 6 trays/hour
Spatial Parallelism

## Slide 93
Latency = ?
Throughput = ?
Temporal Parallelism

## Slide 94
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour
Temporal Parallelism