## Slide 1
Computer System Architectures
Chapter 5
Based on
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 5 :: Topics
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Introduction
Notes: Up to this point, we have examined the design of combinational and sequential circuits using Boolean equations , schematics, and HDLs .
This chapter introduces more elaborate combinational and sequential building blocks used in digital systems. The building blocks are hierarchically assembled from simpler components such as logic gates, multiplexers, and decoders. Each building block has a well defined interface and can be treated as a black box when the underlying implementation is unimportant.

## Slide 4
1-Bit Adders
Notes: Arithmetic circuits are the central building blocks of computers.
Computers and digital logic perform many arithmetic functions: addition, subtraction, comparisons, shifts, multiplication, and division.
Addition is one of the most common operations in digital systems. We begin by building a 1-bit half adder.
As shown in left figure , the half adder has two inputs, A and B, and two outputs, S and Cout.

## Slide 5
1-Bit Adders
Notes: S is the sum of A and B.
If A and B are both 1, S is 2, which cannot be represented with a single binary digit.
Instead, it is indicated with a carry out Cout in the next column.

## Slide 6
1-Bit Adders
Notes: The half adder can be built from an XOR gate and an AND gate.
A full adder accepts the carry in Cin as shown in right Figure.
The figure also shows the output equations for S and Cout.

## Slide 7
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
  Symbol
Multibit Adders (CPAs)
Notes: An N-bit adder sums two N-bit inputs, A and B, and a carry in Cin to produce an N-bit result S and a carry out Cout.
It is commonly called a carry propagate adder (CPA) because the carry out of one bit propagates into the next bit.

## Slide 8
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
Ripple-Carry Adder
Notes: The simplest way to build an N-bit carry propagate adder is to chain together N full adders.
The Cout of one stage acts as the Cin of the next stage, as shown in figure for 32-bit addition.
This is called a ripple-carry adder.
It is a good application of modularity and regularity: the full adder module is reused many times to form a larger system.
The ripplecarry adder has the disadvantage of being slow when N is large.

## Slide 9
tripple = NtFA
where tFA is the delay of a full adder
Ripple-Carry Adder Delay
Notes: The delay of the adder, triple grows directly with the number of bits, as given in equation, where tFA is the delay of a full adder.

## Slide 10
Compute carry out (Cout) for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Column i will generate a carry out if Ai AND Bi are both 1.
  Gi = Ai Bi
    Column i will propagate a carry in to the carry out if Ai OR Bi is 1.
  Pi = Ai + Bi
    The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1
Carry-Lookahead Adder
Notes: The fundamental reason that large ripple-carry adders are slow is that the carry signals must propagate through every bit in the adder.
A carry-lookahead adder (CLA) is another type of carry propagate adder that solves this problem by dividing the adder into blocks and providing circuitry to quickly determine the carry out of a block as soon as the carry in is known.
Thus it is said to look ahead across the blocks rather than waiting to ripple through all the full adders inside a block.

## Slide 11
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate block
Carry-Lookahead Addition

## Slide 12
Example: 4-bit blocks (G3:0 and P3:0) :
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )
  P3:0 = P3P2 P1P0
Generally,
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj )
  Pi:j = PiPi-1 Pi-2Pj
  Ci = Gi:j + Pi:j Ci-1
Carry-Lookahead Adder
Notes: For example, a 32-bit adder may be divided into eight 4-bit blocks.

## Slide 13
32-bit CLA with 4-bit Blocks
Notes: All of the CLA blocks compute the single-bit and block generate and propagate signals simultaneously.

## Slide 14
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16
Carry-Lookahead Adder Delay
Notes: Thus, an N-bit adder divided into k-bit blocks has a delay> For N > 16, the carry-lookahead adder is generally much faster than the ripple-carry adder.
However, the adder delay still increases linearly with N.

## Slide 15
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Å Bi) Å Ci
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages
Prefix Adder
Notes: Prefix adders extend the generate and propagate logic of the carrylookahead adder to perform addition even faster. They first compute G and P for pairs of columns, then for blocks of 4, then for blocks of 8, then 16, and so forth until the generate signal for every column is known.
The sums are computed from these generate signals.

## Slide 16
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin, P-1 = 0
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai Å Bi) Å Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)
Prefix Adder

## Slide 17
Generate and propagate signals for a block spanning bits i:j:
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry
Prefix Adder

## Slide 18
Prefix Adder Schematic
Notes: The network of black cells is called a prefix tree.

## Slide 19
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)
Prefix Adder Delay
Notes: In summary, the prefix adder achieves a delay that grows logarithmically rather than linearly with the number of columns in the adder.
This speedup is significant, especially for adders with 32 or more bits, but it comes at the expense of more hardware than a simple carry-lookahead adder.

## Slide 20
Compare delay of: 32-bit ripple-carry, carry-lookahead, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
Adder Delay Comparisons

## Slide 21
Compare delay of: 32-bit ripple-carry, carry-lookahead, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns
Adder Delay Comparisons

## Slide 22
Subtracter
Notes: Recall that adders can add positive and negative numbers using two’s complement number representation.
Subtraction is almost as easy: flip the sign of the second number, then add.
Flipping the sign of a two’s complement number is done by inverting the bits and adding 1.

## Slide 23
Comparator: Equality
Notes: A comparator determines whether two binary numbers are equal or if one is greater or less than the other.
A comparator receives two N-bit binary numbers A and B.
There are two common types of comparators.
An equality comparator produces a single output indicating whether A is equal to B (A == B).
A magnitude comparator produces one or more outputs indicating the relative values of A and B.

## Slide 24
Comparator: Less Than

## Slide 25
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Arithmetic Logic Unit (ALU)
Notes: An Arithmetic/Logical Unit (ALU) combines a variety of mathematical and logical operations into a single unit.
For example, a typical ALU might perform addition, subtraction, magnitude comparison, AND, and OR operations.
The ALU forms the heart of most computer systems
The control signal F specifies which function to perform.
Control signals will generally be shown in blue to distinguish them from the data.

## Slide 26
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
ALU Design
Notes: The figure shows an implementation of the ALU.

## Slide 27
Compare delay of: 32-bit ripple-carry, carry-lookahead, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns
Adder Delay Comparisons

## Slide 28
Configure 32-bit ALU for SLT operation: A = 25 and B = 32
Set Less Than (SLT) Example

## Slide 29
Configure 32-bit ALU for SLT operation: A = 25 and B = 32
  A < B, so Y should be 32-bit representation of 1 (0x00000001)
  F2:0 = 111
    F2 = 1 (adder acts as subtracter), so 25 - 32 = -7
    -7 has 1 in the most significant bit (S31 = 1)
    F1:0 = 11 multiplexer selects Y = S31 (zero extended) = 0x00000001.
Set Less Than (SLT) Example

## Slide 30
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 =
  Ex: 11001 << 2 =
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb).
  Ex: 11001 >>> 2 =
  Ex: 11001 <<< 2 =
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 =
  Ex: 11001 ROL 2 =
Shifters
Notes: Shifters and rotators move bits and multiply or divide by powers of 2.
As the name implies, a shifter shifts a binary number left or right by a specified number of positions.
There are several kinds of commonly used shifters:

## Slide 31
Logical shifter:
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter:
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator:
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 32
Shifter Design

## Slide 33
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 34
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result
Multipliers
Notes: Multiplication of unsigned binary numbers is similar to decimal multiplication but involves only 1’s and 0’s.
Figure compares multiplication in decimal and binary.
In both cases, partial products are formed by multiplying a single digit of the multiplier with the entire multiplicand.
The shifted partial products are summed to form the result.

## Slide 35
4 x 4 Multiplier
Notes: In general, an N × N multiplier multiplies two N-bit numbers and produces a 2N-bit result.

## Slide 36
4 x 4 Divider
A/B = Q + R/B
Algorithm:
R’ = 0
for i = N-1 to 0
R = {R’ << 1. Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R’=R
Notes: Binary division can be performed using the following algorithm for N-bit unsigned numbers in the range [0, 2^(N−1)]: The partial remainder R is initialized to 0. The most significant bit of the dividend A then becomes the least significant bit of R. The divisor B is repeatedly subtracted from this partial remainder to determine whether it fits. If the difference D is negative (i.e., the sign bit of D is 1), then the quot ient bit Qi is 0 and the difference is discarded. Otherwise, Qi is 1, and the partial remainder is updated to be the difference.
The delay of an N-bit array divider increases proportionally to N^2 because the carry must ripple through all N stages in a row before the sign is determined and the multiplexer selects R or D. This repeats for all N rows.
Division is a slow and expensive operation in hardware and therefore should be used as infrequently as possible.

## Slide 37
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 38
Two common notations:
  Fixed-point: binary point fixed
  Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions
Notes: This section introduces fixed- and floating-point number systems that can represent rational numbers.
Fixed-point numbers are analogous to decimals; some of the bits represent the integer part, and the rest represent the fraction.
Floating-point numbers are analogous to scientific notation, with a mantissa and an exponent.

## Slide 39
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers
Notes: Fixed-point notation has an implied binary point between the integer and fraction bits, analogous to the decimal point between the integer and fraction digits of an ordinary decimal number.

## Slide 40
Represent 7.510 using 4 integer bits and 4 fraction bits.
Fixed-Point Number Example

## Slide 41
Represent 7.510 using 4 integer bits and 4 fraction bits.
  01111000
Fixed-Point Number Example

## Slide 42
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  Two’s complement:
Signed Fixed-Point Numbers

## Slide 43
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers

## Slide 44
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Floating-Point Numbers
Notes: Floating-point numbers are analogous to scientific notation. They circumvent the limitation of having a constant number of integer and fractional bits, allowing the representation of very large and very small numbers.
Like scientific notation, floating-point numbers have a sign, mantissa (M), base (B), and exponent (E).

## Slide 45
Example: represent the value 22810 using a 32-bit floating point representation
We show three versions –final version is called the IEEE 754 floating-point standard
Floating-Point Numbers

## Slide 46
Convert decimal to binary (don’t reverse steps 1 & 2!):
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Floating-Point Representation 1

## Slide 47
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Floating-Point Representation 2

## Slide 48
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Floating-Point Representation 3

## Slide 49
Write -58.2510 in floating point (IEEE 754)
Floating-Point Example

## Slide 50
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Floating-Point Example

## Slide 51
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
Floating-Point: Special Cases

## Slide 52
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
Floating-Point Precision

## Slide 53
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)
Floating-Point: Rounding

## Slide 54
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Floating-Point Addition

## Slide 55
Add the following floating-point numbers:
0x3FC00000
0x40500000
Floating-Point Addition Example

## Slide 56
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Floating-Point Addition Example

## Slide 57
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Floating-Point Addition Example

## Slide 58
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Floating Point Addition Example

## Slide 59
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing
Counters
Notes: This section examines sequential building blocks, including counters and shift registers. An N-bit binary counter, shown in figure, is a sequential arithmetic circuit with clock and reset inputs and an N-bit output Q.
Reset initializes the output to 0.
The counter then advances through all 2^N possible outputs in binary order, incrementing on the rising edge of the clock.

## Slide 60
Implementation:
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Shift Registers
Symbol:
Notes: A shift register has a clock, a serial input Sin, a serial output Sout, and N parallel outputs Q.
On each rising edge of the clock, a new bit is shifted in from Sin and all the subsequent contents are shifted forward.
A shift register can be constructed from N flip-flops connected in series.
Shift registers can be viewed as serial-to-parallel converters.
The input is provided serially (one bit at a time) at Sin.
After N cycles, the past N inputs are available in parallel at Q.

## Slide 61
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)
Shift Register with Parallel Load

## Slide 62
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address
Memory Arrays
Notes: The previous sections introduced arithmetic and sequential circuits for manipulating data.
Digital systems also require memories to store the data used and generated by such circuits.
Registers built from flip-flops are a kind of memory that stores small amounts of data.
This section describes memory arrays that can efficiently store large amounts of data.

## Slide 63
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M
Memory Arrays

## Slide 64
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100
Memory Array Example

## Slide 65
Memory Arrays

## Slide 66
Z
Memory Array Bit Cells
Notes: Memory arrays are built as an array of bit cells, each of which stores 1 bit of data.
Each bit cell is connected to a wordline and a bitline.
For each combination of address bits, the memory asserts a single wordline that activates the bit cells in that row.
When the wordline is HIGH, the stored bit transfers to or from the bitline.
Otherwise, the bitline is disconnected from the bit cell.
The circuitry to store the bit varies with memory type.
To read a bit cell, the bitline is initially left floating (Z).
Then the wordline is turned ON, allowing the stored value to drive the bitline to 0 or 1.
To write a bit cell, the bitline is strongly driven to the desired value.
Then the wordline is turned ON, connecting the bitline to the stored bit.
The strongly driven bitline overpowers the contents of the bit cell, writing the desired value into the stored bit.

## Slide 67
0
1
Z
Z
Memory Array Bit Cells

## Slide 68
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once
Memory Array
Notes: Figure shows the internal organization of a 4 × 3 memory array.
Of course, practical memories are much larger, but the behavior of larger arrays can be extrapolated from the smaller array.
During a memory read, a wordline is asserted, and the corresponding row of bit cells drives the bitlines HIGH or LOW.
During a memory write, the bitlines are driven HIGH or LOW first and then a wordline is asserted, allowing the bitline values to be stored in that row of bit cells.
For example, to read Address 10, the bitlines are left floating, the decoder asserts wordline2, and the data stored in that row of bit cells (100) reads out onto the Data bitlines.
To write the value 001 to Address 11, the bitlines are driven to the value 001, then wordline3 is asserted and the new value (001) is stored in the bit cells.

## Slide 69
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile
Types of Memory
Notes: Memories are classified based on how they store bits in the bit cell.
The broadest classification is random access memory (RAM) versus read only memory (ROM).
RAM is volatile, meaning that it loses its data when the power is turned off.
ROM is nonvolatile, meaning that it retains its data indefinitely, even without a power source.

## Slide 70
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)
RAM: Random Access Memory
Notes: RAM is called random access memory because any data word is accessed with the same delay as any other.
In contrast, a sequential access memory, such as a tape recorder, accesses nearby data more quickly than faraway data.

## Slide 71
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.
ROM: Read Only Memory
Notes: ROM is called read only memory because, historically, it could only be read but not written.
These names are confusing, because ROMs are randomly accessed too.

## Slide 72
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters
Types of RAM

## Slide 73
Invented DRAM in 1966 at IBM
Others were skeptical that the idea would work
By the mid-1970’s DRAM in virtually all computers
Robert Dennard, 1932 -

## Slide 74
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value
DRAM
Notes: Upon a read, data values are transferred from the capacitor to the bitline.
Upon a write, data values are transferred from the bitline to the capacitor.
Reading destroys the bit value stored on the capacitor, so the data word must be restored (rewritten) after each read.

## Slide 75
DRAM
Notes: As shown in Figure (a), when the capacitor is charged to VDD, the stored bit is 1; when it is discharged to GND (Figure b), the stored bit is 0.
The capacitor node is dynamic because it is not actively driven HIGH or LOW by a transistor tied to VDD or GND.

## Slide 76
SRAM
Notes: Static RAM (SRAM, pronounced “es-ram”) is static because stored bits do not need to be refreshed.
Figure shows an SRAM bit cell. The data bit is stored on cross-coupled inverters.
When the wordline is asserted, both nMOS transistors turn on, and data values are transferred to or from the bitlines.

## Slide 77
DRAM bit cell:
SRAM bit cell:
Memory Arrays Review

## Slide 78
ROM: Dot Notation
Notes: Read only memory (ROM) stores a bit as the presence or absence of a transistor.
To read the cell, the bitline is weakly pulled HIGH. Then the wordline is turned ON.
If the transistor is present, it pulls the bitline LOW. If it is absent, the bitline remains HIGH.
Note that the ROM bit cell is a combinational circuit and has no state to “forget” if power is turned off.
The contents of a ROM can be indicated using dot notation.
A dot at the intersection of a row (wordline) and a column (bitline) indicates that the data bit is 1.
For example, the top wordline has a single dot on Data1, so the data word stored at Address 11 is 010.

## Slide 79
Developed memories and high speed circuits at Toshiba, 1971-1994
Invented Flash memory as an unauthorized project pursued during nights and weekends in the late 1970’s
The process of erasing the memory reminded him of the flash of a camera
Toshiba slow to commercialize the idea; Intel was first to market in 1988
Flash has grown into a $25 billion per year market
Fujio Masuoka, 1944 -

## Slide 80
ROM Storage
Notes: Conceptually, ROMs can be built using two-level logic with a group of AND gates followed by a group of OR gates.

## Slide 81
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
ROM Logic

## Slide 82
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 83
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B
Example: Logic with ROMs

## Slide 84
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0
Logic with Any Memory Array

## Slide 85
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 86
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B
Logic with Memory Arrays

## Slide 87
Called lookup tables (LUTs): look up output at each input combination (address)
Logic with Memory Arrays
Notes: Although they are used primarily for data storage, memory arrays can also perform combinational logic functions.
Memory arrays used to perform logic are called lookup tables (LUTs).
Figure shows a 4-word × 1-bit memory array used as a lookup table to perform the function Y= AB.
Each address corresponds to a row in the truth table, and each data bit corresponds to an output value.

## Slide 88
Port: address/data pair
3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory
Multi-ported Memories
Notes: Digital systems often use a number of registers to store temporary variables.
This group of registers, called a register file, is usually built as a small, multiported SRAM array, because it is more compact than an array of flip-flops.

## Slide 89
// 256 x 3 memory module with one read/write port
module dmem( input logic clk, we,
input logic[7:0] a
input logic [2:0] wd,
output logic [2:0] rd);
logic [2:0] RAM[255:0];
assign rd = RAM[a];
always @(posedge clk)
if (we)
RAM[a] <= wd;
endmodule
SystemVerilog Memory Arrays

## Slide 90
PLAs (Programmable logic arrays)
  AND array followed by OR array
  Combinational logic only
  Fixed internal connections
FPGAs (Field programmable gate arrays)
  Array of Logic Elements (LEs)
  Combinational and sequential logic
  Programmable internal connections
Logic Arrays
Notes: Programmable logic arrays (PLAs) implement two-level combinational logic in sum-of-products (SOP) form.
PLAs are built from an AND array followed by an OR array. For example, ROMs can be viewed as a special case of PLAs.
A field programmable gate array (FPGA) is an array of reconfigurable gates.
Using software programming tools, a user can implement designs on the FPGA using either an HDL or a schematic.
FPGAs are more powerful and more flexible than PLAs for several reasons.
They can implement both combinational and sequential logic.

## Slide 91
X = ABC + ABC
Y = AB
PLAs

## Slide 92
PLAs: Dot Notation

## Slide 93
Composed of:
  LEs (Logic elements): perform logic
  IOEs (Input/output elements): interface with outside world
  Programmable interconnection: connect LEs and IOEs
  Some FPGAs include other building blocks such as multipliers and RAMs
FPGA: Field Programmable Gate Array
Notes: FPGAs are built as an array of configurable logic elements (LEs), also referred to as configurable logic blocks (CLBs).
Each LE can be configured to perform combinational or sequential functions.
The LEs are surrounded by input/output elements (IOEs) for interfacing with the outside world.
LEs can connect to other LEs and IOEs through programmable routing channels.

## Slide 94
General FPGA Layout
Notes: This figure shows a general block diagram of an FPGA.

## Slide 95
Composed of:
  LUTs (lookup tables): perform combinational logic
  Flip-flops: perform sequential logic
  Multiplexers: connect LUTs and flip-flops
LE: Logic Element

## Slide 96
Altera Cyclone IV LE

## Slide 97
The Spartan CLB has:
  1 four-input LUT
  1 registered output
  1 combinational output
Altera Cyclone IV LE

## Slide 98
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example

## Slide 99
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB
LE Configuration Example

## Slide 100
Using a CAD tool (such as Altera’s Quartus II)
  Enter the design using schematic entry or an HDL
  Simulate the design
  Synthesize design and map it onto FPGA
  Download the configuration onto the FPGA
  Test the design
FPGA Design Flow